## Slide 1: Dynamic Operating Envelopes
Athul Jose P
11867566

## Slide 2: Introduction
Increased renewable installation at distribution level
Opportunity to participating in markets
To prevent network violations – curtail generation
Unutilized installed capacity of DERs
Operating Envelopes
Dynamic Operating Envelopes
DEIP, “Dynamic operting envelopes working group outcomes report,” DEIP, Tech. Rep., 2022.

## Slide 3: Dynamic Operating Envelope (DOE)
Operating envelopes are the limits that an electricity customer can import and export to the electricity grid
Dynamic Operating Envelopes (DOEs) are where import and export limits can vary over time and location.
DOEs could be used to manage ’flexible loads’ such as water heaters, battery storage and electric vehicles (EVs)
Benefits
1. More solar / battery support 2. Market Efficiency 3. Greater Interoperability 4. Network Efficiency
DEIP, “Dynamic operting envelopes working group outcomes report,” DEIP, Tech. Rep., 2022.

## Slide 4: Calculating DOE
M. Z. Liu, L. N. Ochoa, S. Riaz, P. Mancarella, T. Ting, J. San, and J. Theunissen, “Grid and market services from the edge: Using operating envelopes to unlock network-aware bottom-up flexibility,” IEEE Power and Energy Magazine, vol. 19, no. 4, pp. 52–62, 2021.
Runs series of power flow to explore different combinations of export/imports
OEs are generated for each time period (15 min) in the horizon of interest (6 h)
Different forecasting methods or advanced metering can be added to improve performance of OEs

## Slide 5
Allocation of DOE
M. Alam, P. T. Nguyen, L. Naranpanawe, T. K. Saha, and G. Lankeshwara, “Allocation of dynamic operating envelopes in distribution networks: Technical and equitable perspectives,” IEEE Transactions on Sustainable Energy, 2023.
Two stage approach to allocate DOE
  Distribution System State Estimation (DSSE)
  Capacity Constrained State Optimization (CCSO)
Top-down approach and DOEs calculated at MV-LV transformer points
Optimal distribution of allocated DOEs among DOE-enabled customers ensuring reasonable fairness
DOEs generated at 5/10 min interval

## Slide 6: DOE Control Framework
Y. Z. Gerdroodbari, M. Khorasany, and R. Razzaghi, “Dynamic pq operating envelopes for prosumers in distribution networks,” Applied Energy, vol. 325, p. 119757, 2022.
Control of allocated DOEs is included
Prosumers can independently manage their assets without direct involvement of third party

## Slide 7
DOE with Decomposition Method
M. Mahmoodi, L. Blackhall, S. M. N. RA, A. Attarha, B. Weise, and A. Bhardwaj, “Der capacity assessment of active distribution systems using dynamic operating envelopes,” IEEE Transactions on Smart Grid, 2023
DOEs is defined by non empty convex set
Right Hand Side Decomposition Method is superior in allocation of joint resource shares and independent sectors
As the no of DOEs increases, method produce less wider DOEs

## Slide 8
DOE based Market for Prosumers
M. I. Azim, G. Lankeshwara, W. Tushar, R. Sharma, M. R. Alam, T. K. Saha, M. Khorasany, and R. Razzaghi, “Dynamic operating envelope-enabled p2p trading to maximise financial returns of prosumers,” IEEE Transactions on Smart Grid, 2023
Network aware P2P trading is developed utilizing cooperative game theory
Different power export capabilities
  Self sufficient
  Clean energy
  Profit

## Slide 9: Comparison and Relation to EE 521
Use of power flow, state estimation and optimal power flow to calculate DOEs
Paper | Content
1 | Introduction to DOE and calculation
2 | Complete steps to calculate DOE
3 | DOE based control framework
4 | DOE with decomposition method
5 | DOE based market for prosumers

## Slide 10: Summary
DOEs are used for greater network efficiency and more market operation of DERs
Main component of DOE is checking the network violations from power flow
DOEs can be used with prosumers for electricity markets and shown to be efficient